Ch#8:  Robot Control With Distance Detection
Ch#8: Robot Control With Distance Detection

---
Chapter Goals if approximate distances can be detected
Chapter Goals if approximate distances can be detected
- Make your boe bot follow a moving object while keeping a fixed distance from it
- Follow a black line on a white floor

---
Activity #1:  Sweeping frequencies
Activity #1: Sweeping frequencies
Detector most sensitive at 38500 Hz
  - Objects can be detected at larger distances….sensitivity makes up for reduced intensity
Sensitivity is less above and below this 38500 Hz
  - When less sensitive frequencies pulsed, object must be closer, so intensity makes up for sensitivity.

---
Build the following circuits
Build the following circuits

---
Frequency sensitivity can be used to sense distance
Frequency sensitivity can be used to sense distance

---
Using a simple algorithm to determine a zone
Using a simple algorithm to determine a zone
Each frequency representing each zone will be sent
  - If detection occurs in that zone, “0” is added to a variable
  - If detection does not occur in that zone, “1” is added to that variable
  - ZONE = “The final value of that variable”

---
Example of zone detection
Example of zone detection
Remember, bs2 reports 0 if there is a detection and 1 if there is no detection

---
Another example
Another example

---
The program that you will use includes a new PBASIC command: LOOKUP index,[value0,value1,…..],variable
The program that you will use includes a new PBASIC command:
LOOKUP index,[value0,value1,…..],variable
- If the index argument is 0, value 0 is selected from the list and loaded into the variable following the brackets.
- If the index argument is 2, value2 is selected from the list and loaded into the variable

---
Programming the bs2 to scan these zones and compute the zone
Programming the bs2 to scan these zones and compute the zone

---
- Save and run the program
- Use a sheet of paper to see that the zone value changes with distance
  - Start with the paper 1 cm away, “Zone 0 or 1 will be reported”
  - Gradually move away from the IR LED and be sure the zone value increases with distance

---
Check to be sure that the other side works as well
Check to be sure that the other side works as well
Replace these two lines
  FREQOUT 8,1, irFrequency
  irDetect = IN9
- With these two lines
FREQOUT 2,1,irFrequency
irDetect = IN0

---
Now Let’s Display both distances Enter, Run, and Save the following:
Now Let’s Display both distances
Enter, Run, and Save the following:

---
Activity #2:  Boe-Bot Shadow Vehicle
Activity #2: Boe-Bot Shadow Vehicle
Goal: Make one boe-bot follow another
- If shadow vehicle starts falling behind the leader then it should speedup
- If shadow vehicle gets too close, it should slow down
- If the distance is just right, make no change until it is too close or lagging behind again

---
Control System
Control System
- Software and hardware that is designed to maintain a certain value…in this case a distance or “Zone”
- Here we will use what is called “Closed Loop Control”…

---
Proportional Control Block Diagram for right servo and IR LED-Detector Pair
Proportional Control Block Diagram for right servo and IR LED-Detector Pair

---
Proportional Control Block Analysis
Proportional Control Block Analysis
- Set Point: Zone to maintain (Zone 2)
- Detect Current distance
    - Zone 4
Summing Junction
    - Error= Set Point – Current distance
    - 2 – 4 = -2
Operator block
(Multiply error by proportional constant (kp)
    - Output Adjust = Constant x error
    - -2*35 = -70
Summing Junction
  - Output Adjust + 750 = 680
Pulse new value to right servo
THUS BOE BOT WILL SPEED UP, AND UPDATE STATUS AGAIN
THE CORRECTION WILL ALWAYS BE PROPORTIONAL TO THE ERROR “PROPORTIONAL CONTROL”

---
Here are the equations that will make up the control block
Here are the equations that will make up the control block
ERROR = Right zone set point – measured right zone
OUTPUT ADJUST = Error X 35
RIGHT SERVO OUTPUT =Output Adjust + 750
OR ALL TOGETHER:
Right Servo Output = (Right zone setpoint – measured right zone) x 35 +750

---
Accommodating the left wheel
Accommodating the left wheel
Equation for right wheel:
Right Servo Output = (Right zone set point – measured right zone) x 35 +750
Sample: RSO = (2-4)*35+750 = 680
Equation for left wheel
Left Servo Output = (Left Zone Set point – measured left zone) x -35 + 750
Sample: LSO = (2-4)*-35+750 = 820
NOW BOTH WHEELS WILL ROLL FORWARDAT THE SAME SPEED MAKING THE BOE BOT GO STRAIGHT…ASSUMING THE OBJECT IS RIGHT IN FRONT

---
Enter, Run, & Save FollowingBoeBot.bs2
Enter, Run, & Save FollowingBoeBot.bs2

---
Use a piece of paper to lead your shadow bot around the room
Use a piece of paper to lead your shadow bot around the room
The boe-bot should follow the paper:
  - It will move forward when you pull it away
  - It will turn left when you turn the paper left
  - It will turn right when you turn the paper right
  - It should back up when you move the paper toward it

---
Neat Activity
Neat Activity
All robots should be running “FollowingBoeBot.bs2”
(These bots should have paper plates taped to their backs)
Line up the bots, back to front
Now we should have one boe bot leading a chain of 6 or 7 shadow boe-bots

---
Making some modifications
Making some modifications
- Try changing the Kpr & Kpl constants to numbers from 15 to 50
- Try making adjustments to the SetPoint…try values from 0 to 4

---
Activity #3 Following A Stripe
Activity #3 Following A Stripe
Goal: Make boe-bot follow a stipe of electrical tape on one of the robo arenas

---
Modify Boe-Bot Circuits
Modify Boe-Bot Circuits
Point your IR Pairs downward and outward as shown below

---
Circuit Modifications cont’d
Circuit Modifications cont’d
We will need the IR Light emitted to be a bit dimmer
    - Replace the 1 kohm resistors (Br,Bk,R) powering you IR LEDs with 2 kohm resistors (R,Bk,R)

---
Run DisplayBothDistances.bs2
Run DisplayBothDistances.bs2
Place your boe bot on the robo arena so it is only seeing white.
    - Verify zone readings indicate that arena is detected in a very close zone (zone 1 or zone 0)
Now move your boe bot to a position where both pairs are picking up black tape
    - Zone reading of “4” or “5” should now be detected

---
Now make boe bot straddle the line (One wheel on each side of line)
Now make boe bot straddle the line
(One wheel on each side of line)
Both detectors pairs should be reporting either “Zone 1” or “Zone 2”
  - If the readings are higher, point the IR Detectors slightly further out away from the edge of the stripe
Now the boe bot should be moved left and right until one or the other detectors are focused on the stripe. Verify that one Zone is 4 or 5 while the other is Zone 1 or 2
  - Adjust your detectors until your boe bot passes this test as well

---
Programming Stripe Following Boe Bot
Programming Stripe Following Boe Bot
- Open FollowingBoeBot.bs2 and save it as StripeFollowingBoeBot.bs2
- Change the SETPOINT CON from 2 to 3
- Change Kpl from -35 to 35
- Change Kpr from 35 to -35

---
Save and Run StripeFollowingBoeBot.bs2
Save and Run StripeFollowingBoeBot.bs2
- Place your Boe-Bot at “Start”.
- Put your hand in front of the robot until it moves past the start stripe.
- See if your Boe-Bot follows the stripe.
- When your Boe-Bot sees the “Finish” stripe it should stop and wait there.
- Try different Set Point values and make notes on your Boe-Bot’s performance.

---
Project Stripe following Race
Project
Stripe following Race
- You will be given part of the period to optimize your robot’s performance.
- COMPETITION: Fastest through the line following course gets 1 point added to their graded project for this chapter