Chapter 7: Navigating with Infrared Headlights
Chapter 7: Navigating with Infrared Headlights

---
Infrared
Infrared

---
The Electromagnetic Spectrum
The Electromagnetic Spectrum

---
Infrared Headlights
Infrared Headlights
Close white objects will reflect the light back to the sensor best.

---
Parts and Assembly
Parts and Assembly

---
Circuit
Circuit

---
Add Red LED’s to your breadboard.  When the detector detects reflected IR light, your program will make the corresponding LED light
Add Red LED’s to your breadboard. When the detector detects reflected IR light, your program will make the corresponding LED light
Connect one red LED to pin 10
  - Protect it with a 470 ohm resistor
  - Place it near the left detector
Connect the other red LED to pin 1
  - Protect it with a 470 ohm resistor
  - Place it near the right detector

---
Boe Bot with IR and Visible LEDs
Boe Bot with IR and Visible LEDs

---
To use the sensor:
  - FREQOUT to the IR LEDs at 38,500 Hz for 1 ms
  - Record the detector's output as a variable.
The key is to send a 1 ms 38.6khz signal, then immediately store the IR DETECTORS output as a variable:

---
Infrared is abundant around us (emitted as part of heat from many objects – including us).
But, objects do not emit it on and off at 38,500Hz.
The detector will ignore any source of IR except at that frequency.
RF systems and FM and AM radio work the same way – Our detector ignores these sources because they pulse at frequencies other than 38500 Hz.

---
Enter, Run, and Save TestIrPairsAndIndicators.bs2 below…
Enter, Run, and Save TestIrPairsAndIndicators.bs2 below…

---
Check your IR emitters & detectors
Check your IR emitters & detectors
- Use the debug terminal to verify that the bs2 receives a “0” from each IR detector when an object is placed in front of it.
- Verify that the LED next to each detector emits light when the detector detects an object

---
Remote Testing & Ranges testing
Remote Testing & Ranges testing
- Unplug the boe bot, put switch on “1” not “2”
- Take Boe Bot to a variety of objects and test the range of the detectors
- Try detection range of different colored objects
  - Which colors are detected at the furthest range?
  - Which colors are detected at the closest range

---
Make your Boe-Bot Near Sighted  by changing the resistor in series with one IR LED with the following, recording the maximum distance detected by that IR LED’s detector each time….use a white piece of paper to reflect the IR
Make your Boe-Bot Near Sighted by changing the resistor in series with one IR LED with the following, recording the maximum distance detected by that IR LED’s detector each time….use a white piece of paper to reflect the IR

---
Place the 1kohm resistor in series with the IR LED and get ready to make your BOE-BOT Navigate
ACTIVITY #4: Object detection and avoidance
Place the 1kohm resistor in series with the IR LED and get ready to make your BOE-BOT Navigate
Be sure your detectors and emitters are bent slightly outward as shown to the right.

---
Use your own subroutines with the code below and test your Boe-Bot
Use your own subroutines with the code below and test your Boe-Bot
For “Forward_pulse” use For counter = 1 to 1

---
Now make your red LEDs respond to detection again….to do this add the following lines of code between pause 20 and next for each subroutine:
Now make your red LEDs respond to detection again….to do this add the following lines of code between pause 20 and next for each subroutine:

---
SENSITIVITY
SENSITIVITY
You may notice that your robot is too sensitive and responds too far in advance.
  - There are two solutions to this problem:
    - Hardware: Replace the 1k ohm resistors with 4.7k ohm resistors
    - Software: Put the 1k ohm resistors back and change the frequency from 38500 Hz to 37500 Hz or Less

---
ACTIVITY #5: High Performance IR Navigation
ACTIVITY #5: High Performance IR Navigation
Lets make the boe bot check for objects between every pulse sent to the servos
  - This should allow us to avoid collisions with objects

---
Enter, Run, and Save FastIrRoaming.bs2 below
Enter, Run, and Save FastIrRoaming.bs2 below

---
Notice that pause 20 has been changed to pause 15.
  - Reason: it take about 5 ms to pulse IR LED’s and check the detectors

---
Correcting the problem with corners
Correcting the problem with corners
Modify FastIrRoaming.bs2, so the boe bot makes a 90 degree turn when both Detectors see an obstacle.
  - See next slide for this code…..call it FastIrRoamingModified.bs2
  - Notice how Red LED’s will report when an obstacle has been detected

---
FastIrRoamingModified.bs2

---
Try experimenting with this program further
Try experimenting with this program further
Examples
  - Modify the value of “pulsecount” in some or all of the IF and ELSEIF statements.
  - Modify the values of “PULSELEFT” and/or “PULSERIGHT” in some or all of the IF and ELSEIF statements.

---
See if you can modify the “pulseleft” and “pulseright” values so that the boe bot does everything at half speed
See if you can modify the “pulseleft” and “pulseright” values so that the boe bot does everything at half speed

---
ACTIVITY #6:  The Drop Off Detector
ACTIVITY #6: The Drop Off Detector
GOAL: Make boe bot take evasive action when no object is detected that is “No Ground in front of boe-bot!!”
  - Continue forward so long as both ir detectors can see the surface of the table.

---
Preparing Robot for Drop off detection
Preparing Robot for Drop off detection
- Point IR LED’s and DETECTORS downward and outward
- Place 3 strips of black electrical tape around the border of the “Robo Arena”
- Make boe-bot nearsighted
  - Replace 1kohm resistors with 2 kohm resistors (these are the resistors in series with the IR LED’s)
Use TestIrPairsAndIndicators.bs2 to be sure that the boe-bot detects the arena, but not the tape (Note: Hold the boe-bot in your hand while you do this)

---
Programming Goal:
Programming Goal:
- Roll forward if both detectors send “0”
- Turn away from a detector that reports no object detection “1”
  - If right detector receives “1” and left “0”, turn left
  - If left detector receives “1” and right “0”, turn right
Pulse once between checking, but if drop off detected pulse several times evasively.
  - Control this with a pulse count that is set by the true condition.

---
Enter, Run, And Save, AvoidTableEdge.bs2…Note:  you will have to also declare 6 variables
Enter, Run, And Save, AvoidTableEdge.bs2…Note: you will have to also declare 6 variables