Navigating
the Boe-Bot

---
Overview
Overview
- Reference
- Navigation Intro
- Dead Reckoning
- Line Following
- Wall Following
- Distance Sensing
- Dead Reckoning in Detail
- Moving Forward
- Using Servo Data
- Sample Program
- Bot Travel Distance
- Summary
Boe-Bot Navigation

---
Reference
Reference
- For more complete reference the following are available from:
- http://www.parallax.com/
- http://mfranzen.ca/pages/cor/tej2o1_u3.html#u3a3
- Robotics with the BOEBOT Version 2.2
- BASIC Stamp Syntax and Reference Manual Version 2.1

---
Navigation Intro
Navigation Intro
There are several ways to navigate a course using a robot. A variety of sensors are available to help the robot accomplish this task. Methods for navigating the a course might include:
Dead reckoning
  - Exact path must be known ahead of time
  - Program tells the robot how far to travel before each turn
  - Errors in distances and turning angles accumulate, so best for simple, short courses.
  - Distances can be calculated using servos or stepper motors or infrared sensors can be used to count wheel revolutions.
Line following
  - Requires a line to follow (some factories use lines on the floors that robots follow to deliver parts to assembly workers).
  - Infrared sensors (or other types) shine a beam of light on the floor and determine the line position by the amount of reflection.
Wall following
  - Requires that a wall is available for the robot to touch or sense.
  - One method involves using whiskers – sensors that can tell when the robot touches the wall.
Distance sensing
  - Requires that walls are available so that the robot can sense the distance to each wall.
  - Range-finding sensors can be used to determine the distance to walls beside or in front of the robot.

---
Navigation: Dead Reckoning
Navigation: Dead Reckoning
3 ft
6 ft
Finish
Line
Track to be navigated
Possible path to follow
Go straight for 6 ft
Turn right 90 degrees
Go straight for 3 ft
Turn right 90 degrees
etc
Errors begin to build
Each time that a distance is off or an angle for a turn is off, the robot gets further off the desired path.

---
Navigation: Line Following
Navigation: Line Following
Rounded corners are easier to follow
Tape on track
Line on track
Robot
Infrared light reflects off of the floor
Wheel
Infrared sensor

---
Navigation: Wall Following
Navigation: Wall Following
Path of robot
Place where left whisker hits the wall
Robot naturally drives slightly to the left and then corrects right after left whisker hits the wall
Areas of difficulty?
Right
Whisker
Adding angled barriers to corners may make navigation easier

---
Navigation: Distance Sensing
Navigation: Distance Sensing
Beams from distance sensors
One possible programming approach:
- Steer more to the right if distance A < 2”
- Steer more to the left if distance B < 2”
- Turn right if distance C < 8”
- Keep track of turns (R, R, R, L, L, L, R to complete the course)
A
B
C

---
Dead Reckoning in Detail
Dead Reckoning in Detail
First of all, let’s be sure that it is clear what is meant by LEFT, RIGHT, FORWARD, and BACKWARD with the BOE-BOT. The Robotics Version 2.2 manual indicates that the ping-pong ball wheel is considered to be a rear wheel, so movement is defined as shown below.

---
Moving Forward
Moving Forward
Note that in order for the BOE-BOT to move forward:
- the right wheel must turn clockwise (CW)
- the left wheel must turn counter clockwise (CCW)

---
Using Servo Data
Using Servo Data
In the last team assignment, data was gathered so that servo speed and direction could be determined as PULSOUT Duration is varied. The data might look something like the tables shown below.
Left Wheel Servo
Right Wheel Servo
PULSOUT Duration	Servo speed and direction
650	30 rpm CW
660	27 rpm CW
670	24 rpm CW
680	21 rpm CW
690	18 rpm CW
700	15 rpm CW
710	12 rpm CW
720	9 rpm CW
730	6 rpm CW
740	3 rpm CW
750	0 rpm (Stop)
760	3 rpm CCW
770	6 rpm CCW
780	9 rpm CCW
790	12 rpm CCW
800	15 rpm CCW
810	18 rpm CCW
820	21 rpm CCW
830	24 rpm CCW
840	27 rpm CCW
850	30 rpm CCW
PULSOUT Duration	Servo speed and direction
650	30 rpm CW
660	27 rpm CW
670	24 rpm CW
680	21 rpm CW
690	18 rpm CW
700	15 rpm CW
710	12 rpm CW
720	9 rpm CW
730	6 rpm CW
740	3 rpm CW
750	0 rpm (Stop)
760	3 rpm CCW
770	6 rpm CCW
780	9 rpm CCW
790	12 rpm CCW
800	15 rpm CCW
810	18 rpm CCW
820	21 rpm CCW
830	24 rpm CCW
840	27 rpm CCW
850	30 rpm CCW
Since the BOE-BOT will travel forward if the left servo turns CCW and the right servo turns CCW, it will travel in a straight line using these two PULSOUT Duration values

---
Sample Program
Sample Program
(similar to the program on p. 125 in Robotics, Version 2.2)
‘ Move the BOE-BOT forward in a straight line
Counter VAR Word
FOR Counter = 1 TO 122
PULSOUT 13, 850	‘Move left wheel CCW at max speed
PULSOUT 12, 650	‘Move right wheel CW at max speed
PAUSE 20	‘Pause for 20 ms
NEXT
Note that the program above assumes that the left servo is connected to P13 and the right servo is connected to P12 as shown to the right (reference: p. 100 in Robotics, Version 2.2)

---
Bot Travel Distance
Bot Travel Distance
How far will the BOE-BOT move?
The manual (Robotics, Version 2.2) says that the program on the previous page will run each servo for about 3 seconds. Let’s see why:
FOR Counter = 1 TO 122
PULSOUT 13, 850	‘sets P13 high for 850*2 us = 1.7 ms
PULSOUT 12, 650	‘sets P12 HIGH for 650*2 us = 1.3 ms
PAUSE 20	‘pause for 20 ms
NEXT
- The total time per loop is 1.7 + 1.3 + 20 = 23 ms plus a small amount of time for the BASIC Stamp to execute the instructions. The BASIC Stamp 2 executes 4000 instructions/second or each instruction takes about 0.25 ms. The five instructions in the loop will take about 1.25 ms, so the total time per loop is really about 24.25 ms.
- So the total time for the program is (24.25 ms/loop)(122 loops) = 2.96 seconds
- If the wheels have a diameter D = 2.5” then the circumference C = D = 7.854”
- If the BOE-BOT servos turn a maximum of 30 rpm, then the distance traveled in 2.96 seconds is
- Distance = (30 rev/min)*(1min/60 sec)*(7.854”/rev)(2.96 sec) = 11.62”

---
Calculating Exact Distances
Calculating Exact Distances
Is it necessary to calculate exact distances ahead of time?
- You could take the time to calculate exact distances, but if time allows, you can adjust values in the program until you experimentally determine the required values.
- Adjusting for a straight line
FOR Counter = 1 TO 122
PULSOUT 13, 850
PULSOUT 12, 650
PAUSE 20
NEXT
- Adjusting for a left turn
FOR Counter = 1 TO 15
PULSOUT 13, 750 ‘Stop the left wheel
PULSOUT 12, 650 ‘Move right wheel CW at full speed
PAUSE 20
NEXT
Adjust this value to change the distance that the BOE-BOT travels
Adjust these values if the BOE-BOT isn’t going exactly straight
Adjust this value to change how long the BOE-BOT continues turning left

---
Summary
Summary
- Different ways to navigate the boe-bot using different sensors with additional programming
- Detailed look at dead reckoning issues such as:
  - Wheel/servo direction,
  - using servo data,
  - sample programming,
  - and methods to accomplish this type of navigation