Circuit Theory
Characteristics, Types, Calculations, Units, & Analysis

---
Resources
Resources
For more complete documentation, the following items are available from:
  - Robotics with the BOEBOT Version 2.2
  - Handouts
  - http://mfranzen.ca/index.html
  - http://www.allaboutcircuits.com/
May 2011

---
Overview
Overview
- Atomic structure of related materials
- Electricity and electron flow
  - Ohms law
  - Power
Circuit Types
  - Series
  - Parallel
  - Combination
Quantities and units of measure
Feb 2013

---
Atomic Structure
Atomic Structure
Conductors
  - Metallic material with high conductivity and has few electrons (copper/silver)
Insulators
  - Non Metallic with low conductivity and has many electrons (plastic/rubber)
Semi-conductors
  - Some electrons with intermediate conductivity (silicon/germanium)
[Speaker Notes: Copper: http://www.saburchill.com/chemistry/visual/atoms/029.html Silicon: http://www.saburchill.com/chemistry/visual/atoms/014.html]

---
Electricity
Electricity
Two theories
  - Conventional
    - Electrons flows from positive to negative
    - Scientists originally used this theory
    - more convenient to use
  - Electron
    - Electrons flows from negative to positive
    - current theory used in electronics
    - most accurate in terms of explanation of this theory
  - Using either theory in circuit analysis,
    - THE ANSWERS COME OUT THE SAME!

---
Electricity
- copper wire is a good conductor and it only has one free electron in its valence shell or ring
- electrons are forced into one end (pressure or voltage) which continues to push adjacent free electrons from one atom to the next and so on (battery)
- The amount/flow of electrons going though this conductor is known as the current
- The larger the conductor size the more electrons can flow through (less resistance) which is known as the resistance
- Understanding this theory sums up electricity as:
  - The controlled and directed flow of free electrons from atom to atom in a conductor

---
Ohms Law
Ohms Law
All circuits have common traits
  - Pressure = Voltage E
  - Flow = Current A
  - Restriction = Resistance R
Using the water hose analogy, how these traits relate can be easily understood (E=I*R)
  - With a water hose attached to an outlet, the valve acts as the pressure, the hose size as the restriction, and the water is the flow
  - Turn the valve on half a turn, pressure, and water flow are present
  - Turn the valve to full turn, pressure doubles, and water flow also doubles
  - Now if someone steps on the hose allowing only a quarter flow of the water through, pressure also will drop, but the amount/flow of water will be the same (just slower because of the restriction)

---
Power
Power
- Power in general is the measure of how much work can be done in a given amount of time
- In electric circuits it is a function of both voltage and current similar where Voltage is the specific work (or potential energy) per unit charge, while current is the rate at which electric charges move through a conductor
- Power is equal to the Voltage times the Current (P=E*I), similar to ohms law and is measured in Watts (W)
[Speaker Notes: http://www.allaboutcircuits.com/vol_1/chpt_2/3.html]

---
Circuit Types
Circuit Types
Series Circuits
  - Current has only one path to flow
Parallel Circuits
  - Current has more than one path to flow
Complex Circuits
  - Combination of series and parallel paths for current to flow

---
Ohms Law
- A simple circuit with a power supply, switch (not necessary to draw in) and a single load/resistance
- Calculations are used to troubleshoot, double check, and understand what is happening in an electrical circuit
- With E=I*R, you can use a graphic triangle formula to figure out which formula to use if two of the three variables are known

---
Series Circuits
Series Circuits
- In a series circuit with multiple loads/resistances and only one path, you will find these formulas work if you have one variable missing
- Total voltage is the sum of the individual voltage drops
  - ET = E1 + E2 + E3 …
Total current is equal as there is only one path
  - IT = I1 = I2 = I3 …
Total resistance is the sum of all individual resistances
  - RT = R1 + R2 + R3 …
- Each load is identified by a subscript
- Use a EIRP Table to find solutions easily
[Speaker Notes: Sample calculations using tables: http://aplusphysics.com/wordpress/regents/tag/virp-table/]

---
Series Cct. Calculation Sample
Series Cct. Calculation
Sample
- Here is an sample done by a student showing the basic steps
- Shows given info, diagram, EIRP table (without the Power), rough calculations, and double check

---
Parallel Circuits
Parallel Circuits
- In a parallel circuit with multiple loads/resistances and more than one path, you will find these formulas work if you have one variable missing
- The potential difference across all branches of a parallel circuit must have the same amount
  - ET = E1 = E2 = E3 …
Total current in a parallel circuit is equal to the sum of the currents in the separate branches
  - IT = I1 + I2 + I3 …
The reciprocal of the equivalent resistance is equal to the sum of the reciprocals of the separate resistances in parallel
  - RT = 1 1 1 …
  R1 + R2 + R3
- Each load is identified by a subscript
- Use a EIRP Table to find solutions easily
[Speaker Notes: Sample calculations using tables: http://aplusphysics.com/wordpress/regents/tag/virp-table/]

---
Parallel Cct. Calculation Sample
Parallel Cct. Calculation
Sample
- Here is an sample done by a student showing the basic steps
- Shows given info, diagram, EIRP table (without the Power), rough calculations, and double check

---
Complex Series-Parallel Circuits
Complex Series-Parallel Circuits
- These circuits must be broken down and analyzed into their respective series and parallel components
- Do this by redrawing the circuit by reducing it down to it’s basic series and parallel components one step at a time
  - As you break it down, you calculate the related circuit types
  - Show your steps also in your EIRP table by making more columns
For more detail steps see:
  - http://www.allaboutcircuits.com/vol_1/chpt_7/2.html
[Speaker Notes: http://www.allaboutcircuits.com/vol_1/chpt_7/2.html http://nwscc.cc.al.us/nsfdc/technology/Circuit%20Solutions.htm]

---
Sample Complex Circuit Analysis
Sample Complex Circuit Analysis

---
Quantity, Units, & Symbols
Quantity, Units, & Symbols
It is important to use the right quantities, units and symbols in order to properly calculate solutions
Quantity	Symbol	Unit of Measure	Symbol	Effect in a cct.
EMF or Electromotive force or Voltage or potential	E	Volt	V	Force producing electron flow in a circuit
Resistance or that which is against current flow	R	Ohm		Opposition to the flow of electrons
Current or how much	I	Ampere	A	The Flow of electrons through a circuit
Energy/work done	P	Watt	W	Work/energy used based on voltage and current

---
Units of Measure
Units of Measure
- In the electronic industry, it is often necessary to use very large numbers possibly in the millions or very small numbers such as one millionth
- Using a prefix representing another size will reduce errors and having to write out very large or very small numbers
PREFIX	SYMBOL	MULTIPLIER	EXPONENT
exa	E	1, 000, 000, 000, 000, 000, 000	1018
pera	P	1, 000, 000, 000, 000, 000	1015
tera	T	1, 000, 000, 000, 000	1012
giga	G	1, 000, 000, 000	109
mega	M	1, 000, 000	106
kilo	k	1, 000	103
hecto	h	100	102
deca	da	10	101
Basic Unit		1	100
deci	d	0.1	10-1
centi	c	0.01	10-2
milli	m	0. 001	10-3
micro		0. 000, 001	10-6
nano	n	0. 000, 000, 001	10-9
pico	p	0. 000, 000, 000, 001	10-12
femto	f	0. 000, 000, 000, 000, 001	10-15
atto	a	0. 000, 000, 000, 000, 000, 001	10-18

---
Common Units of Measure
Common Units of Measure
- Prefixes commonly used in electronic/electrical industry are as shown in the tables
- When calculating solutions, always ensure you are working with the same units of measure
- Example: 8, 000 W = ? kW
= 8 * 0.001
= 8 kW
	micro	milli	units	kilo	Mega
micro		0.001	10-6	10-9	10-12
milli	1, 000		0.001	10-6	10-9
units	106	1, 000		0.001	10-6
kilo	109	106	1, 000		0.001
Mega	1012	109	106	1, 000
Prefix	Mega	kilo	Decimal Point	milli	micro
Symbol	M	k	.	m	
Relation to base unit	1, 000, 000	1, 000	1	0.001 or 1/1, 000	0.000, 001 or 1/1, 000, 000
Example	5 M	8 kV	12 V,A or 	6 mV	12 A
Pronounced	5 Megaohms / (5, 000 k or 5, 000, 000 )	8 kilovolts / (0.008 MV or / 8, 000 V)	Volts / Amps / Ohms	6 millivolts / (0.006 V)	12 microamps / (0.012 mA or / 0.000, 012 A)
# of spaces from decimal	6	3	0	3	6

---
Calculation Requirements
Calculation Requirements
In order to prove (get full marks) the solution, the following must be included in your assignments:
  - Circuit diagram showing simplified line diagram with symbols and given information
  - EIRP Table – with answers circled
  - Rough Calculations showing:
    - Order of Operation
    - Formula
    - Substitution
    - Units on all variables
    - Rounded off to two decimals after units of measure are applied
    - All answers circled
  - Include final double check, using a formula that you have not yet used confirming solution works

---
More Formulas
More Formulas
These are more formulas derived from the original Ohms law formula E=I*R