Circuits
Circuits
Current
Resistance & Ohm’s Law
Resistors in Series, in Parallel, and in combination
Capacitors in Series and Parallel
Voltmeters & Ammeters
Resistivity
Power & Power Lines
Fuses & Breakers
Bulbs in Series & Parallel

---
Electricity
Electricity
The term electricity can be used to refer to any of the properties that particles, like protons and electrons, have as a result of their charge. Typically, though, electricity refers to electrical current as a source of power. Whenever valence electrons move in a wire, current flows, by definition, in the opposite direction. As the electrons move, their electric potential energy can be converted to other forms like light, heat, and sound. The source of this energy can be a battery, generator, solar cell, or power plant.

---
Current
Current
By definition, current is the rate of flow of positive charge. Mathematically, current is given by:
If 15 C of charge flow past some point in a circuit over a period of 3 s, then the current at that point is 5 C/s. A coulomb per second is also called an ampere and its symbol is A. So, the current is 5 A. We might say, “There is a 5 amp current in this wire.”
It is current that can kill a someone who is electrocuted. A sign reading “Beware, High Voltage!” is really a warning that there is a potential difference high enough to produce a deadly current.
I =
q
t

---
Charge Carriers & Current
Charge Carriers & Current
A charge carrier is any charged particle capable of moving. They are usually ions or subatomic particles. A stream of protons, for example, heading toward Earth from the sun (in the solar wind) is a current and the protons are the charge carriers. In this case the current is in the direction of motion of protons, since protons are positively charged. In a wire on Earth, the charge carriers are electrons, and the current is in the opposite direction of the electrons. Negative charge moving to the left is equivalent to positive charge moving to the right. The size of the current depends on how much charge each carrier possesses, how quickly the carriers are moving, and the number of carriers passing by per unit time.
protons
I
wire
electrons
I

---
A Simple Circuit
A circuit is a path through which an electricity can flow. It often consists of a wire made of a highly conductive metal like copper. The circuit shown consists of a battery ( ), a resistor ( ), and lengths of wire ( ). The battery is the source of energy for the circuit. The potential difference across the battery is V. Valence electrons have a clockwise motion, opposite the direction of the current, I. The resistor is a circuit component that dissipates the energy that the charges acquired from the battery, usually as heat. (A light bulb, for example, would act as a resistor.) The greater the resistance, R, of the resistor, the more it restricts the flow of current.
A Simple Circuit

---
Building Analogy
Building Analogy
To understand circuits, circuit components, current, energy transformations within a circuit, and devices used to make measurements in circuits, we will make an analogy to a building.
Continued…
I
R
V

---
Building Analogy Correspondences
Building Analogy Correspondences
Battery ↔ Elevator that only goes up and all the way to the top floor
Voltage of battery ↔ Height of building
Positive charge carriers ↔ People who move through the building
        en masse (as a large group)
Current ↔ Traffic (number of people per unit time moving past
        some point in the building)
Wire w/ no internal resistance ↔ Hallway (with no slope)
Wire w/ internal resistance ↔ Hallway sloping downward slightly
Resistor ↔ Stairway, ladder, fire pole, slide, etc. that only goes down
Voltage drop across resistor ↔ Length of stairway
Resistance of resistor ↔ Narrowness of stairway
Ammeter ↔ Turnstile (measures traffic without slowing it down)
Voltmeter ↔ Tape measure (for measuring changes in height)

---
Current and the Building Analogy
Current and the Building Analogy
In our analogy people correspond to positive charge carriers and a hallway corresponds to a wire. So, when a large group of people move together down a hallway, this is like charge carriers flowing through a wire. Traffic is the rate at which people are passing, say, a water fountain in the hall. Current is rate at which positive charge flows past some point in a wire. This is why traffic corresponds to current.
Suppose you count 30 people passing by the fountain over a 5 s interval. The traffic rate is 6 people per second. This rate does not tell us how fast the people are moving. We don’t know if the hall is crowded with slowly moving people or if the hall is relatively empty but the people are running. We only know how many go by per second. Similarly, in a circuit, a 6 A current could be due to many slow moving charges or fewer charges moving more quickly. The only thing for certain is that 6 coulombs of charge are passing by each second.

---
Battery & Resistors and the Building Analogy
Battery & Resistors and the Building Analogy
Our up-only elevator will only take people to the top floor, where they have maximum potential and, thus, where they are at the maximum gravitational potential. The elevator “energizes” people, giving them potential energy. Likewise, a battery energizes positive charges. Think of a 10 V battery as an elevator that goes up 10 stories. The greater the voltage, the greater the difference in potential, and the higher the building. As reference points, let’s choose the negative terminal of the battery to be at zero electric potential and the ground floor to be at zero gravitational potential. Continued…
top floor hallway: high Ugrav
elevator
flow of
+ charges
+
flow of
people
R
V
-
bottom floor hallway: zero Ugrav
staircase

---
Battery & Resistors and the Building (cont.)
Battery & Resistors and the Building (cont.)
Current flows from the positive terminal of the battery, where + charges are at high potential, through the resistor where they give up their energy as heat, to the negative terminal of the battery, where they have zero potential energy. The battery then “lifts them back up” to a higher potential. The charges lose no energy moving the a length of wire (with no internal resistance). Similarly, people walk from the top floor where they are at a high potential, down the stairs, where their potential energy is converted to waste heat, to the bottom floor, where they have zero potential energy. The elevator them lifts them back up to a higher potential. The people lose no energy traveling down a (level) hallway.
top floor hallway: high Ugrav
elevator
flow of
+ charges
+
flow of
people
R
V
-
bottom floor hallway: zero Ugrav
staircase

---
Resistance
Resistance
Resistance is a measure of a resistors ability to resist the flow of current in a circuit. As a simplistic analogy, think of a battery as a water pump; it’s voltage is the strength of the pump. A pipe with flowing water is like a wire with flowing current, and a partial clog in the pipe is like a resistor in the circuit. The more clogged the pipe is, the more resistance it puts up to the flow of water trying to flow through it, and the smaller that flow will be. Similarly, if a resistor has a high resistance, the current flowing it will be small. Resistance is defined mathematically by the equation:
V = I R
Resistance is the ratio of voltage to current. The current flowing through a resistor depends on the voltage drop across it and the resistance of the resistor. The SI unit for resistance is the ohm, and its symbol is capital omega: Ω. An ohm is a volt per ampere:
1 Ω = 1 V / A
The Voltage Lab (scroll down)

---
Resistance and Building Analogy
Resistance and Building Analogy
In our building analogy we’re dealing with people instead of water molecules and staircases instead of clogs. A wide staircase allows many people to travel down it simultaneously, but a narrow staircase restricts the flow of people and reduces traffic. So, a resistor with low resistance is like a wide stairway, allowing a large current though it, and a resistor with high resistance is like a narrow stairway, allowing a smaller current.
I = 4 A
I = 2 A
R = 3 Ω
R = 6 Ω
V = 12 V
V = 12 V
Narrow staircase means reduced traffic.
Wide staircase means
more traffic.

---
Ohm’s Law
Ohm’s Law
The definition of resistance, V = I R, is often confused with Ohm’s law, which only states that the R in this formula is a constant. In other words, the resistance of a resistor is a constant no matter how much current is flowing through it. This is like saying a clog resists the flow of water to the same extent regardless of how much water is flowing through it. It is also like saying a the width of a staircase does not change: no matter what rate
people are going downstairs, the stairs hinder their progress to the same extent. In real life, Ohm’s law is not exactly true. It is approximately true for voltage drops that aren’t too high. When voltage drops are high, so is the current, and high current causes more heat to generated. More heat means more random thermal motion of the atoms in the resistor. This, in turn, makes it harder for current to flow, so resistance goes up. In the circuit problems we do we will assume that Ohm’s law does hold true.
Georg Simon Ohm
    1789-1854

---
Ohmic vs. Nonohmic Resistors
Ohmic vs. Nonohmic Resistors
If Ohm’s law were always true, then as V across a resistor increases, so would I through it, and their ratio, R (the slope of the graph) would remain constant.
In actuality, Ohm’s law holds only for currents that aren’t too large. When the current is small, not much heat is produced in a real, so resistance is constant and Ohm’s law holds (linear portion of graph). But large currents cause R to increase (concave up part of graph).
V
V
I
I
Ohmic Resistor
Real Resistor
ohmic
non-ohmic

---
Series & Parallel Circuits
Series & Parallel Circuits
When several circuit components are arranged in a circuit, they can be done so in series, parallel, or a combination of the two.
Resistors in Series
Resistors in Parallel
I
I
R1
V
R2
V
R1
R2
R3
R3
Voltage drops can be different; they sum to V.
Each voltage drop is identical and equal to V.
Current going through each resistor is the same and equal to I.
Current going through each
resistor can be different; they
sum to I.

---
Resistors in Series: Building Analogy
Resistors in Series: Building Analogy
R1
R1
R2
Elevator (battery)
R2
R3
3 steps
To go from the top to the bottom floor, all people must take the same path. So, by definition, the staircases are in series. With each flight people lose some of the potential energy given to them by the elevator, expending all of it by the time they reach the ground floor. So the sum of the V drops across the resistors the voltage of the battery. People lose more potential energy going down longer flights of stairs, so from V = I R, long stairways correspond to high resistance resistors.
The double waterfall is like a pair of resistors in series because there is only one route for the water to take. The longer the fall, the greater the resistance.
6 steps
11 steps

---
Equivalent Resistance in Series
Equivalent Resistance in Series
If you were to remove all the resistors from a circuit and replace them with a single resistor, what resistance should this replacement have in order to produce the same current? This resistance is called the equivalent resistance, Req. In series Req is simply the sum of the resistances of all the resistors, no matter how many there are:
Req = R1 + R2 + R3 + · · ·
Mnemonic: Resistors in Series are Really Simple.
I
I
R1
V
V
Req
R2
R3

---
Proof of Series Formula
Proof of Series Formula
V1 + V2 + V3 = V (energy losses sum to energy gained by battery)
V1= I R1, V2= I R2, and V3= I R3 ( I is a constant in series)
I R1 + I R2 + I R3 = I Req ( substitution)
R1 + R2 + R3 = Req ( divide through by I )
I
I
}
R1
V1
V
}
V
Req
V2
R2
}
R3
V3

---
Series Sample
Series Sample
4 
1. Find Req
12 
2. Find Itotal
0.5 A
3. Find the V drops across
each resistor.
2 V, 1 V, and 3 V
(in order clockwise from top)
Solution on next slide
6 V
2 
6 

---
Series Solution
Series Solution
1. Since the resistors are in series, simply add
    the three resistances to find Req:
Req = 4  + 2  + 6  = 12 
4 
2. To find Itotal (the current through the battery), use V = I R:
6 = 12 I. So, I = 6/12 = 0.5 A
3. Since the current throughout a series
    circuit is constant, use V = I R with each
    resistor individually to find the V drop
    across each. Listed clockwise from top:	V1 = (0.5)(4) = 2 V
V2 = (0.5)(2) = 1 V
V3 = (0.5)(6) = 3 V
Note the voltage drops sum to 6 V.
6 V
2 
6 

---
Series Practice
Series Practice
1. Find Req
6 
17 
2. Find Itotal
0.529 A
1 
3. Find the V drop across each
   resistor.
9 V
V1 = 3.2 V
V2 = 0.5 V
7 
V3 = 3.7 V
V4 = 1.6 V
check: V drops sum to 9 V.
3 

---
Resistors in Parallel: Building Analogy
Resistors in Parallel: Building Analogy
R2
Elevator (battery)
R1
Suppose there are two stairways to get from the top floor all the way to the bottom. By definition, then, the staircases are in parallel. People will lose the same amount of potential energy taking either, and that energy is equal to the energy the acquired from the elevator. So the V drop across each resistor equals that of the battery. Since there are two paths, the sum of the currents in each resistor equals the current through the battery. A wider staircase will accommodate more traffic, so from
V = I R, a wide staircase corresponds to a resistor with low resistance.
The double waterfall is like a pair of resistors in parallel because there are two routes for the water to take. The wider the fall, the greater the flow of water, and lower the resistance.

---
Equivalent Resistance in Parallel
Equivalent Resistance in Parallel
I1 + I2 + I3 = I (currents in branches sum to current through battery )
V = I1 R1, V = I2 R2, and V = I3 R3 (V is a constant in parallel)
V
V
V
V
+
+
=
(substitution)
R1
R2
Req
R3
1
1
1
1
(divide through by V )
+
+
=
R1
R2
Req
R3
This formula extends to any number of resistors in parallel.
I
I1
I2
I3
I
V
R1
R2
R3
V
Req

---
Parallel Example
Parallel Example
1. Find Req
2.4 
2. Find Itotal
6.25 A
6 
15 V
4 
3. Find the current
    through, and voltage
    drop across, each
    resistor.
It’s a 15 V drop across each. Current in middle branch is 3.75 A; current in right branch is 2.5 A. Note that currents sum to the current through the battery.
Solution on next slide

---
Parallel Solution
Parallel Solution
Itotal
I2
1. 1/Req= 1/R1 + 1/R2 = 1/4 + 1/6
= 6/24 + 4/24 = 5/12
Req = 12/5 = 2.4 
I1
6 
4 
15 V
2. Itotal = V / Req
= 15 / (12/5)
= 75/12 = 6.25 A
3. The voltage drop across each resistor is the same in parallel.
    Each drop is 15 V. The current through the 4  resistor is
   (15 V)/(4 ) = 3.75 A. The current through the 6  resistor is
   (15 V)/(6 ) = 2.5 A. Check:
Itotal = I1 + I2

---
Parallel Practice
Parallel Practice
1. Find Req
48/13  = 3.69 
2. Find Itotal
13/2 A
24 V
3. Find the current
    through, and voltage
    drop across, each
    resistor.
I1 = 2 A
I2 = 1.5 A
I3 = 3 A
V drop for each is 24 V.
12 
16 
8 

---
Combo Sample
Combo Sample
1. Find Req
8.5 
2. Find Itotal
1.0588 A
3. Find the current through,
    and voltage drop across, the
    highlighted 9 V resistor.
Hint: First find the V drop
over the 4  resistor next to the battery. This resistor is in series with the rest of the circuit. Subtract this V drop from that of the battery to find the remaining drop along any path.
0.265 A, 2.38 V
Solutions …
9 V
4 
9 
4 
5 
18 
18 
18 
Itotal

---
Combo Solution: Req  &  Itotal
Combo Solution: Req & Itotal
We simplify the circuit a section at a time using the series and parallel formulae and use V = I R and the end. The units have been left off for clairy.
Req = 8.5 
9 V
I total =1.0588 A
9
4
9
4
5
18
9
9
4
9
4
5
18
18
18
9
4
18
9
18
9
4
4.5

---
Combo Solution: V  Drops & Current
Combo Solution: V Drops & Current
To find the current in the red resistor we must find the voltage drop across its branch. Working from the simplified circuit on the last slide, we see that the resistor next to the battery is in series with the rest of the circuit, which is a 4.5  equivalent. The total current flows through the 4 , so the V drop across it is 1.0588(4) = 4.235 V. Subtracting from 9 V, this leaves 4.765 V across the 4.5  equivalent. There is the same drop across each parallel branch within the equivalent. We’re interested in the left branch, which has 18  of resistance in it. This means the current through the left branch is 4.765 / 18 = 0.265 A. This is
the current through the red resistor. The voltage drop across it is 0.265(9) = 2.38 V. Note that this is half the drop across the left branch. This must be the case since 9  is half the resistance of this branch.
9
4
4.5
9
4
18
9
18

---
Combo Practice
Combo Practice
Each resistor is 5 , and the battery is 10 V.
1. Find Req
6.111 
2. Find Itotal
1.636 A
R
3. Find the current
    through, and voltage
    drop across, the
    resistor R.
0.36 A
12V
5 
4 
2 
2 
3 
6 
6 

---
Color Code for Resistors
Color Code for Resistors
Color coding is a system of marking the resistance of a resistor. It consists of four different colored bands that are used to figure out the resistance in ohms.
The first two bands correspond to a two-digit number. Each color corresponds to a particular digit that can looked up on a color chart.
The third band is called the multiplier band. This is the power of ten to be multiplied by your two-digit number.
The last band is called the tolerance band. It gives you an error range for the labeled resistance.

---
Color Code Example
Color Code Example
A resistor color code has these color bands: Calculate its resistance and accuracy.
(yellow, green, red, gold)
1. Look up the corresponding numbers for the first three
   colors (at this Color Chart link):
Yellow = 4, Green = 5, Red = 2
2. Combine the first two digits and use the multiplier:
45  102 = 4500
3. Find the tolerance corresponding to gold and calculate the
   maximum error:
Gold = 5% and 0.05(4500) = 225.
So, the resistance is 4500 Ω  225 Ω
Test out color codes by changing resistance: Color Code

---
Resistor Thinking Problem
Resistor Thinking Problem
Schmedrick is building a circuit to run his toy choo-choo-train. To be sure his precious train is
not engulfed in flames, he needs an 11  resistor. Unfortunately, Schmed only has a box of 4  resistors. How can he use these resistors to build his circuit? There are many solutions. Try to find a solution that only uses six resistors. Several solutions follow.

---
Thinking Problem: Simplest Solution
Thinking Problem: Simplest Solution
Putting two 4  resistors
in series gives you 8  of
resistance, and you need 3 
more to get to 11 . With
4 
4 
two 4  resistors in parallel, the pair will have an equivalent of 2  . Putting four 4  resistors in parallel yields 1  of resistance for the group of four. The groups are in series, giving a total of 11 .
4 
4 
4  each
Other solutions…

---
Thinking Problem: Other Solutions
Thinking Problem: Other Solutions
4 + 2 + 2 + 1 + 1 + 1 = 11
4 + 4 + 1 + 1 + 1 = 11

---
Capacitor Review
Capacitor Review
V
As soon as switch S is closed a clock-wise current will flow, depositing positive charge on the right plate, leaving the left plate negative. This current starts out as V / R, but it decays to zero with time because as the charge on the capacitor grows the voltage drop across it grows too. As soon as Vcap= V, the current ceases.
The cap. maintains a charges separation, equal but opposite charges. When S is closed, Q increases from zero to C Vcap. C is the capacitance of the capacitor, its charge storing capacity. The bigger C is, the more charge the cap. can store at a given voltage. At any point in time Q = C Vcap. Even when removed from
S
R
-Q
+Q
C
the circuit, the cap. can maintain its charge separation and result in a shock.
A charged cap. stores electrical potential energy in an electric field between its plates. The battery stores chemical potential energy (chemical reactions supply charge carriers with potential energy). The resistor does not store energy; rather it dissipates energy as heat whenever current flows through it.

---
Capacitors: Series & Parallel Circuits
Capacitors: Series & Parallel Circuits
Like resistors, capacitors can be arranged in series, parallel, or in combo of each. Compare this table to the one for resistors. Note that here charge takes the place of current.
Capacitors in Series
Capacitors in Parallel
C1
V
C1
C2
C2
C3
V
C3
Voltage drops can be different; they sum to V.
Voltage drops are all the same and equal to V.
Charge on each capacitor is the same and equal to Qtotal.
Charge on each capacitor
can be different; they sum
to Qtotal.

---
Parallel Capacitors
Parallel Capacitors
If we removed all capacitors in a circuit and replaced them with a single capacitor, what capaciatance should it have in order to store the same charge as the original circuit? This is called the equivalent capacitance, Ceq. In
parallel the voltage drop across each resistor is the same, just as it was with resistors. Because the capacitances may differ, the charge on each capacitor may differ. From Q = C V:
q1 = C1 V
and q2 = C2 V.
The total charged stored is:
qtotal = q1 + q2. So,
Ceq V = C1 V + C2 V, and
V
qtotal
Ceq = C1 + C2 . In general,
Ceq = C1 + C2 + C3 + ···
Ceq
V
C1
C2
V1 = V
V2 = V
q1
q2

---
Capacitors in Series
Capacitors in Series
V
In series the each capacitor holds the same charge, even if they have different capaci-tances. Here’s why: The battery “rips off ” a charge -q from the right side of C1 and deposits it on the left side of C3. Then the left side of C3 repels a charge -q from its right plate. over to the left side of C2. Meanwhile, the right side of C1 attracts a charge -q from the right side of C2. Charges don’t jump across capacitors, so the green “H” and the blue “H” are isolated and must remain neutral. This forces all capacitors to have the same charge. The total charge is really just q, since this is the only charge acted on by the battery. The inner H’s could be removed and it wouldn’t make a difference.
V3
V2
V1
q
q
q
C3
C1
C2
V
qtotal = q
Ceq

---
Capacitors in Series  (cont.)
Capacitors in Series (cont.)
V
V = V1 + V2 + V3
V3
V2
So, from Q = C V:
V1
q
q
q
C3
C1
C2
(since each the charge on each capacitor
 is the same as the total charge).
 This yields:
V
1
=
qtotal = q
Ceq
In general, for any number in parallel
1
Ceq
1
1
1
+
+
+ ···
=
Ceq
C1
C2
C3
1
C1
C2
+
C3
+
1
1
Ceq
=
C1
C2
+
C3
+
q
q
q
q

---
Capacitor-Resistor Comparison
Capacitor-Resistor Comparison
	V = I R				V = Q (1/C)
	Resistors				Capacitors
	Series	Parallel			Series	Parallel
Currents	same	add		Charges	same	add
Voltages	add	same		Voltages	add	same
Series: Req =  Ri
Series:
Parallel:
Parallel: Ceq =  Ci
“Resistors in Series
 are Really Simple.”
“Parallel Capacitors are
 a Piece of Cake.”
The formulae for series are parallel are reversed simply because in the defining equations at the top, R is replaced with 1/C.
Req
=
1

Ri
1
Ceq
=
1

Ci
1

---
Ammeters
Ammeters
An ammeter measures the current flowing through a wire. In the building analogy an ammeter corresponds to a turnstile. A turnstile keeps track of people as they pass through it over a certain period of time. Similarly, an ammeter keeps track of the amount of charge flowing through it over a period of time. Just as people must go through a turnstile rather than merely passing one by, current must flow through an ammeter. This means ammeters must be installed in a the circuit in series. That is, to measure current you must physically separate two wires or components and insert an ammeter between them. Its circuit symbol is an “A” with a circle around it.
R
R
Ammeter inserted into a circuit in series
If traffic in a hallway decreased due to people passing through a turnstile, the turnstile would affect the very thing we’re asking it to measure--the traffic flow. Likewise, if the current in a wire decreased due to the presence of an ammeter, the ammeter would affect the very thing it’s supposed to measure--the current. Thus, ammeters must have very low internal resistance.

---
Voltmeters
Voltmeters
A voltmeter measures the voltage drop across a circuit component or a branch of a circuit. In the building analogy a voltmeter corresponds to a tape measure. A tape measure measures the height difference between two different parts of the building, which corresponds to the difference in gravitational potential. Similarly, a voltmeter measures the difference in electric potential between two different points in a circuit. People moving through the building never climb up or down a tape measure along a wall; the tape is just sampling two different points in the building as people pass it by. Likewise, we want charges to pass right by a voltmeter as it samples two different points in a circuit. This means voltmeters must be installed in parallel. That is, to measure a
R
V
R
Voltmeter connected in a circuit in parallel
voltage drop you do not open up the circuit. Instead, simply touch each lead to a different point in the circuit. Its circuit symbol is an “V” with a circle around it.
Suppose a voltmeter is used to measure the voltage drop across, say, a resistor. If a significant amount of current flowed through the voltmeter, less would flow through the resistor, and by V = I R, the drop across the resistor would be less. To avoid affecting which it is measuring, voltmeters must have very high internal resistance.

---
Power
Power
Recall that power is the rate at which work is done. It can also be defined as the rate at which energy is consumed or expended:
energy
Power =
time
For electricity, the power consumed by a resistor or generated by a battery is the product of the current flowing through the component and the voltage drop across it:
P = I V
Here’s why: By definition, current is charge per unit time, and voltage is energy per unit charge. So,
energy
charge
energy
I V =

= P
=
time
charge
time

---
Power: SI Units
Power: SI Units
As you probably remember from last semester, the SI unit for power is the watt. By definition:
1 W = 1 J / s
A watt is equivalent to an ampere times a volt:
1 W = 1 A V
(1 C / s) (1 J / C) = 1 J / s = 1 W.
This is true since

---
Power: Other Formulae
Power: Other Formulae
Using V = I R power can be written in two other ways:
P = I V = I ( I R ) = I 2 R
or
P = I V = ( V / R ) V = V 2 / R
In summary,
P = I V,
P = I 2 R,
P = V 2 / R

---
Power Sample Problem
Power Sample Problem
1. What does each meter read?
A1
12V
A1: 6 A, A2: 4 A, A3: 2 A, V: 12 V
3
A2
2. What is the power output of the battery?
A3
6
P = I V = (6 A) (12 V) = 72 W.
The converts chemical potential energy to heat at a rate of 72 J / s.
V
3. Find the power consumption of each resistor.
4. Demonstrate conservation of energy.
Power input = 72 W; Power output = 48 W + 24 W = 72 W.
Middle branch: P = I 2 R = (4 A)2 (3 Ω) = 48 W
Bottom branch: P = I 2 R = (2 A)2 (6 Ω) = 24 W
Bottom check: P = V 2/ R = (12 V)2 / (6 Ω) = 24 W

---
Fuses and Breakers
Fuses and Breakers
fuses
breakers
Fuses and breakers act as safety devices in circuits. They prevent circuit overloads, which might happen when too many appliances are in use. Whenever too much current is being drawn, a fuse will blow or a breaker will trip. This breaks the circuit before the excessive current risks causing a fire.
A fuse has a thin metal filament, like a light bulb. If too much current flows through it, it heats up to the point where it melts, interrupting the flow of current. The fuse must then be replaced. Fuses rated for small currents will have thinner filaments. Breakers are designed to “trip” and switch the circuit off until they are reset.

---
Resistivity & Conductivity
Resistivity & Conductivity
Conductivity is a measure of how well a substance conducts electricity. Resistivity, , is a measure of how well a substance resists the flow of electricity; it is the reciprocal of conductivity. Metals have high conductivity and low resistivity. But even copper, a great conductivity has a small resistivity. So far we have pretended that wires in circuits are perfect conductors, meaning no voltage drops occur over a length of wire. It is usually fine to pretend this is the case unless the wires are extremely long, as in power lines. In real life, the nonzero resistivity of a wire cause it to have some internal resistance, as if a tiny resistor were imbedded within it. In the building analogy this corresponds with a hallway that slopes downward slightly, so people lose a little bit of energy as the walk down the hall.

---
Resistivity & Resistance
Resistivity & Resistance
Resistance is an object property. It represents the degree to which an object resists flow of current. Resistivity is a material property. It represents the degree to which a material comprising an object resists flow of current. Ex: A wire is an object and it has some internal resistance. Copper is common material used to make wire and it has a known, small resistivity. The resistivity of copper is the same in any wire, but different wires have different internal resistances, depending on their lengths and diameters. A wire’s resistance is proportional to its length (imagine every meter of wire with a tiny, built-in resistor) and inversely proportional to its cross-sectional area (just as a wider pipe allows greater flow of water). The constant of proportionality is the resistivity:
R = resistance of the wire
 = resistivity of the metal in wire
L = length of the wire
A = cross sectional area of the wire
R =
 L
A

---
Resistivity:  SI Units
Resistivity: SI Units
The SI unit for resistivity is an ohm-meter: Ω m, as can be deduced from the formula:
Copper has a resistivity of 1.69  10-8 Ω m. The internal resistance of a copper wire depends on how long and how thick it is, but since  is so small, the resistance of the wire is usually negligible.
Resistivity is considered a constant, at least at a given temperature. Resistivity increases slightly with temperature. This is why resistors behave in a nonohmic fashion when the current is high--high current leads to high temperatures, which increases resistivity, which increases resistance.
R =
 L
A

---
Resistivity Practice
Resistivity Practice
12 V
The wire in the circuit the circuit shown is made from
29 cm of copper wire with a diameter of 0.8 mm. The internal resistance of the ammeter is 0.2 . What does the ammeter read?
A
5 
4 
This is like 4 resistors in series with superconducting wire between them.
Rwire =  L / A = (1.69  10-8 Ω m) (0.29 m) / [ (4  10-4 m)2]
        = 9.75  10-3 Ω.
Req = 4 Ω + 5 Ω + 0.2 Ω + 9.75  10-3 Ω = 9.20975 Ω
I = 1.3029 A  1.3 A, about what it would be ignoring the ammeter’s
        and wire’s resistance.

---
Power Lines
Power Lines
Power is transmitted from power plants via power lines using very high voltages. Here’s why: A certain amount of power must be supplied to a town. From P = I V, either current or voltage must high in order to meet the needs of a power hungry town. If the current is high, the power dissipated by the internal resistance of the long wires is significant, since this power is given by
transformer
P = I 2 R. Power companies use high voltage so that the current can be smaller. This minimizes power loss in the line. At your house voltage must be decreased significantly. This is accomplished by a transformer, which can step up or step down voltages.

---
Kilowatt-Hour: An Energy Unit
Kilowatt-Hour: An Energy Unit
The power company measures your energy consumption in a unit called a kilowatt-hour. It is a unit of energy, not power; it is the amount of energy delivered in one hour when the power output is 1 kW. (Power  time = energy.)
For example, if turned on 10 light bulbs, and each is a 100 W bulb, this would use energy at a rate of 1000 J/s or 1000 W. If you leave the bulbs on for an hour, you will have consumed 1 kilowatt-hour of energy.
As its name would imply, a kilowatt-hour is a kilowatt times an hour. Convert 1 kilowatt-hour into megajoules.
3.6 MJ

---
Light Bulbs in Parallel
Light Bulbs in Parallel
Light bulbs are intended and labeled for parallel circuits, since that’s how are homes are wired. Suppose we hook up 3 bulbs of different wattages in parallel as shown. The filament of each bulb acts as a resistor. Each bulb has same potential difference across it, but the currents going the each must be different. Otherwise, they would be equally bright. As you would expect, the 100 W bulb is the brightest. From P = I V, the 100 W bulb must have the highest current going through it (since V is constant). From V = I R, the
100 W bulb must have the filament with the lowest resistance. Note that if one bulb is removed, the others still shine. In summary, in parallel:
I60 < I75 < I100 R100 < R75 < R60 V = constant
I
I60
I75
I100
R60
R75
R100
V
60 W
75 W
100 W

---
Light Bulbs in Series
Light Bulbs in Series
high R,
bright
Let’s place the same 3 bulbs in series now. From P = I 2 R, the power output of any bulb is proportional to its resistance (since each has the same current flowing through it). On the last slide we concluded that bulbs labeled with higher wattages have lower resistances. The resistances of their filaments remain the same no matter how they are wired. This means the 100 W bulb will be the dimmest, and the 60 W bulb will be the brightest. Note that if any bulb is
I
R60
60 W
V
R75
75 W
R100
100 W
low R,
dim
removed now, all bulbs go out. Also note that the power consumption stamped on a bulb is only correct if the bulb is connected in parallel with at a certain voltage. In summary, in series:
P100 < P75 < P60 R100 < R75 < R60 I = constant

---
CREDITS
CREDITS
Ohm picture: http://hubcap.clemson.edu/~asommer/ohm.html
Voltage Lab: http://jersey.voregon.edu.edu/vlab/Voltage/
Color code picture: http://webhome.idirect.com/~jadams/electronic/resist_codes.html
Color Code Link: http://www.electrician.com/resist_calc/resist_calc.htm
Ohm picture: http://hubcap.clemson.edu/~asommer/ohm.html
Voltage Lab: http://jersey.voregon.edu.edu/vlab/Voltage/
Color code picture: http://webhome.idirect.com/~jadams/electronic/resist_codes.html
Color Code Link: http://www.electrician.com/resist_calc/resist_calc.htm