Servo Motors
Boe-Bot

---
Overview
Overview
- Introduction
- Reference
- Boe-Bot Servo
- Servo Applications
- Inside an RC Servo
- Servos/BASIC Stamp
- PBASIC Commands
- Command Examples
- Set-up and Centering
- Speed/RPM Servo Testing
- Graphing Speed/RPM
- Review
Servo Motors on the Boe-Bot

---
Introduction
Introduction
- Servo Motors are DC Motors with a servo mechanism to provide a precise angular motion
- Pulse width modulation (PWM) technique is used to set the angle or speed of rotation
- Although a lot of servo’s are made up differently, similar components can be found in different variations

---
References
References
- The following references may be used for more detailed information:
  - www.parallax.com
  - http://mfranzen.ca/pages/cor/tej2o1_u3.html#u2a2
  - Parallax Manuals:
    - Robotics with the Boe-bot Version 2.2
    - BASIC Stamp Syntax and Reference Manual Version 2.1
[Speaker Notes: http://100rabhagarwal.blogspot.ca/2011/07/servo-motor.html]

---
Servo’s
Servo’s
- Servo Motors are DC Motors with a servo mechanism to provide a precise angular motion
- Pulse width modulation (PWM) technique is used to set the angle of rotation
- Generally RC servo motors have a rotation limit of 900 to 1800 but servos with high rotation angles are also available

---
Servo’s
A servo is a single device that contains:
  - Motor
  - Gearbox that gears down the motor to provide slower speeds (than most motors) and higher torque (power to turn).
  - Built-in electronics such that the motor position or speed can be controlled by a series of pulses. The servo is powered using 5V (4.8 – 6.0 V)

---
RC Servo  Applications
RC Servo
Applications
- Used in many different applications as seen to the right
- Without servo’s robot type control would not be possible
- More common to use servo’s to rotate to a specific angle as opposed to continuous rotation.

---
RC Servo Applications
RC Servo Applications
- Used in more complex type of applications creates some amazing creations
- With appropriate programming, servo’s can accomplish just about anything you need them for
- Boe-bot only uses two continuous servos to drive/navigate, but can use more to accomplish more functions

---
Inside an RC Servo Motor
Inside an RC Servo Motor
Servo is made up of many components

---
Servo - Connections
Servo - Connections
A servo needs three inputs to operate - one for positive voltage, second for ground and third one for PWM (Pulse width modulation)

---
Servo - Electronics
Servo - Electronics
The electronic circuit below consists of the necessary control and feedback components to run the DC motor with the PWM input

---
Servo– Horn/Arm
Servo– Horn/Arm
A servo horn or also known as servo arm which rotates with the motor spindle

---
Servo – Gear Arrangement
Servo – Gear Arrangement
Gears arrangement plays an important role to provide necessary high torque and to provide feedback

---
Servo - Gears
Servo - Gears
Below shows various gears used in a servo motor

---
Servo – Motor & Potentiometer
Servo – Motor & Potentiometer
DC motor and the potentiometer which is used to provide feedback to the electronic circuitry.
It is connected with the DC motor with the help of gear assembly.
As soon as the motor starts rotating the potentiometer also starts rotating and the output of potentiometer i.e. voltage across the middle terminal changes which acts as the feedback signal to indicate the degree of rotation of the motor.

---
Servo Components
Servo Components
Below shows the servo’s major components such as the gears, potentiometer, motor, horn/arm and electronics

---
Metal Gear RC Servo’s
Metal Gear RC Servo’s
- Metal offer strength, increased load and jarred capacity, but are heavier
- Nylon most common with their smooth and light operation
- Karbonite 5 times strength of nylon and better wear resistance
[Speaker Notes: http://www.servocity.com/html/what_servo_do_you_need_.html]

---
A Servo Motor System
A Servo Motor System
Below is a chart showing how a servo motor system works:

---
Types of Servos
Types of Servos
Unmodified servos – the servo can turn over a certain range, such as 180º
  - This type of servo is commonly used on RC (radio control) cars and airplanes for steering, moving control flaps, etc.
  - Most servos are of this type are available in hobby and electronic stores
  - The servo position is controlled by varying the pulse width of a control signal
Modified servos
This type of servo has been modified internally so that it will turn continuously.
This type of servo is useful as a drive motor for a robot, such as the BOE-BOT.
The servo speed is controlled by varying the pulse width of a control signal
0 degrees
90 degrees
180 degrees
0º
90º
180º
Full speed CW
Stop
Full speed CCW
CW
Stop
CCW

---
Controlling Servos With the BASIC Stamp
Controlling Servos With the BASIC Stamp
- As just seen, servos are controlled by varying the pulse width of a control signal.
- This is easily done using the PULSOUT command. Recall that this command was also used to turn ON and OFF an LED with the BOE-BOT in an earlier lab. The form of the PULSOUT command is shown below:
PULSOUT Command
PULSOUT Pin Duration	- this command is used to set the specified Pin
HIGH for a time equal to Duration multiplied by 2 μs.
Example:
PULSOUT 6, 500	- set P5 HIGH for 1000 μs = 1 ms
If the example command above was used in the program shown below, it would produce the waveform shown.
DO
PULSOUT 6, 500 ‘Set P6 HIGH for 1 ms
PAUSE 20 ‘Pause for 20 ms
LOOP ‘ Loop continuously
1 ms
1 ms
P6
20 ms

---
PBASIC Commands
PBASIC Commands
Variables are defined in PBASIC as follows:
VAR Command
Name VAR Size where size can be BIT, NIB, BYTE, or WORD
where
BIT	uses 1 binary digit (bit) to store the value (so the max value is 1)
NIB	uses 4 bits to store the value (so the max value is 11112 = 1510)
BYTE	uses 8 bits to store the value (so the max value is 111111112 = 25510)
WORD	uses 16 bits to store the value (so the max value is 11111111111111112 = 6553510)
Example:
X VAR BYTE
X = 37
Mouse	VAR BIT	‘Value can be 0 or 1
Cat	VAR NIB	‘Value can be 0 to 15
Dog	VAR BYTE	‘Value can be 0 to 255
Rhino	VAR WORD	‘Value can be 0 to 65535
Mouse =	1, Cat =	8, Dog =	48, Rhino =	12345

---
PBASIC Commands
Loops can be created in PBASIC in several manners. If a set of instructions are to be performed a specific number of times, the FOR … NEXT loop is convenient.
FOR … NEXT Loop Command
Count VAR Word ‘Use any variable name to serve as a loop counter
FOR Count = Initial-Value TO Final-Value STEP Increment
List of instructions
NEXT
Example: (What does this program do?)
N VAR BYTE
FOR N = 0 TO 50 STEP 2
DEBUG CR,”HELL0”
NEXT

---
PBASIC Commands
Another example: (What does this program do if an LED is connected to P12?)
Number VAR Word
FOR Number = 0 TO 10	‘The increment equals 1 if STEP is omitted
HIGH 12
PAUSE 1000
LOW 12
PAUSE 1000
NEXT
What is the difference between the two programs shown below?
DO
PULSOUT 6, 500
PAUSE 20
LOOP
M VAR Word
FOR M = 1 TO 100
PULSOUT 6, 500
PAUSE 20
NEXT
Estimate how long the second program will run (recall that the BASIC Stamp 2 executes about 4000 instructions/second so each instruction takes about 0.25 ms, not including any delays specified by the instruction).

---
Controlling the Servo Movement
Controlling the Servo Movement
Servos typically operate by receiving control signals where the pulse width varies from about 1.3 μs to about 1.7ms. So the signals shown below and the corresponding programs can be used to control a servo.
1.3 ms
1.3 ms
P6
20 ms
DO
PULSOUT 6, 650 ‘Set P6 HIGH for 1.3 ms
PAUSE 20 ‘Pause for 20 ms
LOOP ‘ Loop continuously
Full speed CW
1.5 ms
1.5 ms
P6
20 ms
DO
PULSOUT 6, 750 ‘Set P6 HIGH for 1.5 ms
PAUSE 20 ‘Pause for 20 ms
LOOP ‘ Loop continuously
Stop
1.7 ms
1.7 ms
P6
20 ms
DO
PULSOUT 6, 850 ‘Set P6 HIGH for 1.7 ms
PAUSE 20 ‘Pause for 20 ms
LOOP ‘ Loop continuously
Full speed CCW

---
Set-up and Centering the Servos
Set-up and Centering the Servos
- You will need to confirm the servos are centred. To do this you will run a program that sends the servos a signal, instructing them to stay still as they may not be adjusted properly.
- Details for set-up page 60-63 and servo centering page 66-70 of your manual.
DC Power Adaptor Pin Switch	Connect Continuous Servos

---
Set-up and Centering the Servos
Reconnect your 2 LED circuits on P12 & P13 as shown below in Figure 2-15
You will need a small Philips screwdriver and a test program to test each servo separately. Note left & right wiring for servos.

---
Sample Program: Centring the Servo
Sample Program: Centring the Servo
' Robotics with the Boe-Bot - CenterServoP12.bs2
' This program sends 1.5 ms pulses to the right servo connected to' P12 for manual centering.
' {$STAMP BS2}
' {$PBASIC 2.5}
DEBUG "Program Running!“
DO
PULSOUT 12, 750
PAUSE 20
LOOP
Experiment by adjusting carefully the right internal servo potentiometer with the screwdriver and ensure servo is not moving or zeroed, then write a program for P13 and test the left servo and adjust again to center second servo.

---
Speed/RPM Servo Testing
Speed/RPM Servo Testing
PULSOUT Duration	Servo speed and direction
650	40 rpm CW
660	40 rpm CW
670	39 rpm CW
680	37 rpm CW
690	34 rpm CW
700	30 rpm CW
710	25 rpm CW
720	19 rpm CW
730	12 rpm CW
740	3 rpm CW
750	0 rpm (Stop)
760	3 rpm CCW
770	11 rpm CCW
780	18 rpm CCW
790	27 rpm CCW
800	31 rpm CCW
810	35 rpm CCW
820	39 rpm CCW
830	42 rpm CCW
840	42 rpm CCW
850	43 rpm CCW
Pick a number large enough so that you will have time to count the wheel revolutions.
Each servo is a little different from the next, so everyone will test their two servos by varying the pulse width gradually in order to determine the servos speed and direction for each value of Duration used with the PULSOUT Pin Duration command.
Sample Test Program
(servo connected to P13)
FOR N = 1 T0 1000
PULSOUT 13, 650
PAUSE 20
NEXT
Vary the Duration from 650 to 850 and count the wheel revolutions

---
Servo Calibration Testing
Servo Calibration Testing
- You will need to record the number of RPM’s for each PULSOUT comment for each servo. Graph the information (similar to the graphs shown below)
- Your data will be used in later labs to determine which PULSOUT commands are needed to make your BOEBOT move around a pre-determined track

---
Summary
Summary
- Servo is a special motor with very precise speed and control through digital signal and programming
- Lots of applications for servos
- A close up look of what is inside a servo
- Two types of servos, unmodified for specific angle and modified continuous rotation
- PULSOUT can be used with loop commands to control time/distance of servo rotation
- Calibration of servo – centering and speed need to be checked so programming specific tasks can be accomplished